1964 Cessna 182H

N2426R

Limitations

Normal Category

- 2800 pounds

- Flaps up: 3.8g, -1.52 g

- Flaps down: 3.5g

Airspeeds (MPH)

Vso		60

Vs		67

Vx		60 (20° flaps)

70

Vy		90	  (climb 23”/2450 RPM)

Vcc		100-120 (climb 23”/2450 RPM)

Vfe		60-110

Vno		67-170

Vne		193

Va		128

Vglide		80

Traffic Pattern:

Short Takeoff

- 20° Flaps

Abeam

- 13” MP-15” MP

- 10° flaps

- 100 MPH

Base

- 20° flaps

- 90 MPH

Final

- 30° flaps

- 75-80 MPH

Short landing

- 40°flaps

- 70 MPH

Systems

Flaps:

- Electric

- 0-40°

Electrical System

- 14 volt system

- Alternator

Engine

- Continental 0-470-R

- 230 HP@ 2600 RPM

- Normal RPM: 2200-2450 RPM

Caution RPM: 2450-2600 RPM

Max RPM: 2600 RPM

- MP 15-23”

- CHT 275-450°F (Do Not operate above 400°F)

- 10 Quarts Oil/ 8.0-9.0 normal range

- Engine oil pressure 30-60 PSI/10 PSI minimum at idle

- Engine oil temp: 225°F

Fuel System

- 2 tanks/32.5 gallons each

- 30 gallons usable/2.5 gallons unusable per tank

- Takeoff and land on BOTH

- 3 strainers (1 cockpit)

Main wheel

- 32 PSI

Nose wheel

- Do NOT turn more than 29° either direction

- 32 PSI

Weight & Balance

- 2800# Gross weight Normal category

- 1088# useful load

- 120# baggage compartment